## Slide 1: Compartmental Modelling
Dr Mike Chappell
M.J.Chappell@warwick.ac.uk
Structural Identifiability Analysis

## Slide 2: What are compartmental models?
Consist of finite number of compartments
  homogeneous, well-mixed, lumped subsystems
  kinetically the same
Exchange with each other and environment
Inter-compartment transfers represent flow of material
Rate of change of quantity of material in each compartment described by first order ODE
  principle of mass balance
AMR Summer School: Structural Identifiability Analysis

## Slide 3
General form of system equations
where qi denotes quantity in compartment i
fij denotes the flow rate coefficient from i to j
compartment 0 is external environment
AMR Summer School: Structural Identifiability Analysis

## Slide 4: Areas of application of compartmental models
Used extensively in:
  Pharmacokinetics and Anaesthesia (drug kinetics)
  Biomedicine/Biomedical Control (Tumour Targeting)
  Chemical Reaction Systems (Enzyme Chains, Nuclear Reactors)
Also:
  Electrical Engineering (Lumped systems of transmission lines, filters, ladder networks)
  Ecosystems (Ecological Models)
  Neural Computing (Neural Nets)
  Process Industries (Black Box Models)
AMR Summer School: Structural Identifiability Analysis

## Slide 5: Linear (time-invariant) compartmental models
Flow rates, Fij = fij qi
  directly proportional to amount of material in donor compartment, qi (mathematically: fij = kij)
  does not depend on any other amounts
System equations:
where inflow rate f0i has been written as an input/control function ui(t) – external source of material
AMR Summer School: Structural Identifiability Analysis

## Slide 6
General form of system equations
Perhaps an oversimplification, but does provide (in general) good description of responses of many systems when small perturbation (ie: input) is made to system previously in steady state
AMR Summer School: Structural Identifiability Analysis

## Slide 7: Common forms of input for pharmacokinetic models
Mathematical Term
  ui(t)
  Di δ(t) – impulsive input of size Di at time t = 0
  k0i – constant input of size k0i per unit of time
  – repeated . impulsive inputs of size Dij at times tj
Pharmacokinetic Term
  input or intervention
  bolus injection of dose Di .
  constant infusion of drug, rate k0i per unit of time
  repeated bolus injections of dose Dij at times tj
AMR Summer School: Structural Identifiability Analysis

## Slide 8: Rules for compartmental models
General rules
  amounts can’t be negative (positive system), qi ≥ 0
  flows can’t be negative, fij(q)qi ≥ 0
State space form:
  can be written in form q´ = F(q)q + I
  F(q) is compartmental matrix and satisfies
    sum of terms down column i equals elimination from compartment i
    diagonal terms are outflows from respective compartments – so not positive
    off diagonal terms are inflows so not negative
AMR Summer School: Structural Identifiability Analysis

## Slide 9: Example: One compartment model
Examples:
  radioactive substance (decay)
  systemic blood & perfused tissue
System equations
with observation
(c1 is observation gain)
AMR Summer School: Structural Identifiability Analysis

## Slide 10: Example: One compartment model
System equations
Taking Laplace transforms and rearranging
the transfer function relating input to output
AMR Summer School: Structural Identifiability Analysis

## Slide 11: Example: One compartment model
Transfer function:
Impulsive input, u1(t) = D1δ(t)
Constant input, u1(t) = k01
AMR Summer School: Structural Identifiability Analysis

## Slide 12: Example: One compartment model
Observed impulse response of one compartment model
AMR Summer School: Structural Identifiability Analysis

## Slide 13: Example: One compartment model
Observed step (constant infusion) response of one compartment model
AMR Summer School: Structural Identifiability Analysis

## Slide 14: Example: One compartment model
Observed response of one compartment model with repeated bolus injections of size D1 repeated at regular intervals of T
AMR Summer School: Structural Identifiability Analysis

## Slide 15: Exercise: Two compartment model
System equations
?????
with observation
?????
(c1 is observation gain)
AMR Summer School: Structural Identifiability Analysis

## Slide 16: Example: Two compartment model
System equations
with observation
(ci are observation gains)
AMR Summer School: Structural Identifiability Analysis

## Slide 17: Example: Two compartment model
System equations
These can be rewritten in vector-matrix state-space form:
for matrices A, B and C; and so the Transfer Function is given by C (sI – A)-1 B
AMR Summer School: Structural Identifiability Analysis

## Slide 18: Example: Two compartment model
System equations
Note:
So aij = kji (i ≠ j) – off diagonal terms
Diagonal terms:
AMR Summer School: Structural Identifiability Analysis

## Slide 19: Example: Two compartment model
Impulsive input
  Suppose u1(t) = D1δ(t) (and u2(t) = 0)
Constant infusion
  Suppose u1(t) = k01 (and u2(t) = 0)
AMR Summer School: Structural Identifiability Analysis

## Slide 20: Example: Two compartment model
Observed response of two compartment model with impulsive input to compartment 1 (impulse response)
AMR Summer School: Structural Identifiability Analysis

## Slide 21: Example: Two compartment model
Observed response of two compartment model with constant input to compartment 1 (step response)
AMR Summer School: Structural Identifiability Analysis

## Slide 22: Example: One compartment nonlinear model
System equation
Note: Elimination (Michaelis-Menten) saturates
Impulsive input: u1(t) = D1δ(t), treat as q1(0+) = D1
No explicit analytical solution for q1(t)
AMR Summer School: Structural Identifiability Analysis

## Slide 23: Michaelis-Menten saturation curve
AMR Summer School: Structural Identifiability Analysis

## Slide 24: Input response under nonlinear elimination
Impulse response of one compartment nonlinear model with varying input (Km = Vm = b1 = c1 = 1)
AMR Summer School: Structural Identifiability Analysis

## Slide 25: Repeated impulsive inputs under nonlinear elimination
Response to repeated impulsive inputs at regular intervals of 1 time unit with varying input (Km = 12, Vm = 15, b1 = c1 = 1)
(adapted from K. Godfrey. Compartmental Models and their Applications, 1983)
AMR Summer School: Structural Identifiability Analysis

## Slide 26: Model for Tumour Targeting
AMR Summer School: Structural Identifiability Analysis

## Slide 27: Other important considerations
Identifiability of unknown system parameters
  Given postulated system model, values for some of parameters (eg rate constants) may not be known
  Identifiability is a theoretical analysis of whether these parameters may be uniquely determined from perfect input/output data
    Linear systems – relatively straightforward
    Nonlinear systems – fewer methods, complex
Parameter estimation (the real situation)
AMR Summer School: Structural Identifiability Analysis

## Slide 28: Other important considerations
Parameter estimation (the real situation)
  It may be necessary/instructive to actually calculate estimates for unknown parameter values for postulated model from real data (actual measurements/observations)
  Generally performed using computer packages which employ linear/nonlinear regression techniques
  Practical problems for Pharmacokinetic Models:
    Few Data Points (eg blood samples)
    Inaccuracy of Measurement – method of collection (eg urine samples)
    Measurement Noise
AMR Summer School: Structural Identifiability Analysis

## Slide 29
AMR Summer School: Structural Identifiability Analysis