## Slide 1: Disease Diagnostics Data Analysis
Dr James A. Covington
Bio-Medical Sensors Laboratory
School of Engineering

## Slide 2: Sensors@Warwick

## Slide 3: Motivation…
Point of care
Rapid
Patient acceptable
Low-cost
Simple
Hospitals/Home
Developing countries

## Slide 4: The Biological Solution

## Slide 6: Artificial Olfaction
Invented at Warwick in the early 1980s replicate the human nose
Non-invasive, real-time
Immediate sample introduction
Portable/small form factor
Can be used away from the lab
Easy to use/understand
No specialised services (gas lines etc.).
Dr George Dodd

## Slide 7: Electronic Nose Operation
e-
e-
e-
e-
e-
e-
Array of sensors with different broad sensitivity e.g. Alcohols
Operate by measuring change in resistance/capacitance/frequency
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-

## Slide 8: Electronic Nose for Medicine
sensor
array
DRmax / Rb
time
DRmax

The air from around an area of interest is sampled
Many sensors within the electronic nose respond to different odours within the sample. These responses are then processed
Time
Response
Example Sensor Response
Sample in
Sample out

## Slide 9: Understanding your problem…
Disease Diagnostics Data Analysis

## Slide 10: What is the medical question?
Which one is the same as the standard?
Is there any difference
between these two?

## Slide 11: Nature of the test…

## Slide 12: What are the issues?
Who took the sample?
How did they take the sample?
When did they take the sample?
How old is the sample?
Did they take it in a different room?
When did the person last eat?
Do they have perfume on?
When was the room last cleaned?
Understand how your sample is collected

## Slide 13: University Hospital Coventry & Warwickshire
Diseases investigated…
  Bile acid malabsorption
  Bladder/prostate Cancer
  Clostridium difficile
  Coeliac's disease
  Colorectal Cancer
  Crohns disease /Ulcerative colitis
  Diabetes
  Hepatic encephalopathy
  Irritable bowel syndrome
  Liver disease
  Obesity
  Pelvic radiation
  Pre-term labour
  Tuberculosis
Brain Cancer/Schizophrenia
Liver disease
Wound infections
Lung diseases
Metabolic diseases
Eye infections
Ear/Nose/Throat
Bacterial infections
i.e. MRSA & C-Diff
Application of ‘Smell Technology’
Gastrointestinal
diseases

## Slide 14: Understanding your Machine…
Electronic noses in Medicine

## Slide 15: Important Test Conditions

## Slide 16: Traditional Electronic Nose
Array of discrete Sensors
Most employ metal-oxides
Non-linear response with gas concentration
Change in resistance can be defined as:
Where Rs is the sensor resistance, A is a constant and alpha is the slope of the Rs curve

## Slide 17: Typical Sensor Responses
Generates around 1000 data points per sensor
Feature reduction is required

## Slide 18: Potential Features…

## Slide 19: And also…
And anything else you can think of…

## Slide 20: Ion Mobility Spectrometry - FAIMS
Used in chemical warfare detection
Applications for military or home security

## Slide 21: Sample Collection…
Urine
Breath
FAIMS creates datasets of 52,254 data points for one scan
Usually three full scans are taken
Feature reduction is critical…
Stool

## Slide 22: Wavelet transformation
Raw Data
Data in 1D
Discrete
Wavelet transform
Andrea S. Martinez-Vernon 2016

## Slide 23: Wavelet transform
At each level in the above diagram the signal is decomposed into low and high frequencies.
Due to the decomposition process the input signal must be a multiple of 2n where is the number of levels.

## Slide 24: Feature heat-map Coeliac Disease
1 in 100 in the UK are affected, with many undiagnosed
Urine samples used, 20 CD patients and 27 controls
Heat map of different features
Clear differences in the dataset

## Slide 25: Understanding your Data processing…
Disease Diagnostics Data Analysis

## Slide 26: Multivariate data processing techniques

## Slide 27: Unsupervised - PCA example
In PCA, we are interested to find the directions (components) that maximize the variance in our dataset
Linear separation

## Slide 28: Supervised - LDA example
LDA determines a suitable subspace to distinguish between patterns that belong to different classes

## Slide 29: Classifiers - Traditional
Two common are k-Nearest Neighbour and neural networks (with various learning methods)
Multi-output solution
K-NN

## Slide 30: Medical binary classifiers
Single-output solution…many options…
  Support vector machine: Samples are assigned into a new feature space to maximise the difference between the two groups
  Random Forrest: Creates a series of decision trees which vote together to create a classification
  Sparse logistic regression: Fits a model to the data and then uses this model to predict unknown samples (non-linear)
But also…
  Neural network
  Gaussian processes

## Slide 31: Medical binary classifiers II
Support vector machines
Random forest

## Slide 32: FAIMS Medical Data
Remove “zero” values (padding)
Wilcoxon rank-sum test for (with cross-validation) in turn
It is a non-parametric statistical hypothesis test used when comparing two related samples, matched samples, or repeated measurements on a single sample to assess whether their population mean ranks differ (i.e. it is a paired difference test).
Then keep only the features with the lowest p-value
Normally n=2 is sufficient

## Slide 33: Coeliac's from urine
Box whisker plot of probabilities
Boxes show interquartile range
Data created by Sparse Logistic regression
Sensitivity/Specificity of 85%

## Slide 34: What does you medic want you to give them?
Electronic noses in Medicine

## Slide 35: Sensitivity and Specificity
Sensitivity: measures the proportion of positives that are correctly identified
Specificity measures the proportion of negatives that are correctly identified
  True positive: Sick people correctly identified as sick
  False positive: Healthy people incorrectly identified as sick
  True negative: Healthy people correctly identified as healthy
  False negative: Sick people incorrectly identified as healthy

## Slide 36: IBD in Breath
Graphical plot that illustrates the performance of a binary classifier system as its discrimination threshold is varied.
Plots the positive rate (sensitivity) against the false positive rate (specificity) at various threshold settings.
76 IBD patients / 22 Controls
Random Forrest Classifier
Sensitivity: 74%
Specificity: 75%

## Slide 37: C.Diff from Stool
213 stool samples
  All suspected of C.diff
71 confirmed cases
10 fold cross-validation
AUC = 0.93 (95% CI: 0.85,1)
Sensitivity: 92%
Specificity: 86%

## Slide 38: Conclusions…
Electronic noses have been around for more than 20 years
Developed at Warwick, there have been a range of classification approaches applied to them
Critical understanding of the medical problem is needed before processing data
Multiple methods applied to classification – with mixed results
Future maybe a machine in every GP and/or home