## Slide 1
We have described the development of a biosensor consisting of a low-loss SAW biosensor, associated interface circuitry and a biological functional layer of HEK293 cells that was deposited and grown on the SAW devices. Work is under way to instantiate this sensor as a fully integrated analogue VLSI system.
Conclusions and Future work
Biomimetic microsystem for the detection of ratiometrically encoded semiochemicals
M. Cole*1, J. Gardner1, S. Pathak1, M. Chowdhury1, Z. Rácz1 and D. Markovic2, M. Jordan2, J. Challis2
*M.Cole@warwick.ac.uk, 1University of Warwick, Coventry, United Kingdom, 2University of Leicester, Leicester, United Kingdom
Abstract – The development of a novel surface acoustic wave biosensor for liquid phase ligand detection is presented. The functional layer of the biosensor comprises human embryonic kidney cells that efficiently express specific ligand receptors and is coupled to the acousto-electric transducer. A low-loss shear horizontal surface acoustic wave device was developed and fabricated for the detection of receptor-ligand interactions in heterologous systems. The proof of concept implementation of a protocol to immobilize cells expressing insect olfactory receptors on the device surface has been successful. This biological sensor also can be used more generally to monitor cell viability when challenged with toxins, drugs or other substances.
Acknowledgement: This work is supported by the EC Framework 6 IST Programme under iCHEM Project Reference FP6-032275.
Figure 7. Results of the MTT cell viability assay showing that HEK293 can be grown on both LiTaO3 and Au surfaces and the cells do not have a preferred growth region.
Introduction
SAW-based biosensor development
Poly-D-lysine
Nucleus
LiTaO3 substrate
Cell edge
Bilipid layer
Olfactory receptors
VLSI integration
Wind tunnel/Chamber
Chemoreceiver
Classified signal
Bio-reactor
Ratiometric mixing/dilution
Evaporator/
Artificial Gland
Osc. Mixer1
Temperature and
Other Controls
SAW1
Output
Interface
FPGA
Osc. Mixer2
SAW2
Osc. Mixern
SAWn
Chemoemitter
Flash memory
18:CoA
12
OAc
11
OAc
-2c
9
11
OAc
-2c
Q
TD
T
TD
T
TD
T
TD
T
OH
Chemoemitter
Chemoreceiver
WORLD
Concentration Ratios
Concentration Ratios
Blend ratio information
MFC
mass change/optical
electrical
local interneuron
projection neuron
mass flow
synapse
Sensor design
Sensor interface circuitry
200 μm
20 μm
2.5 μm
Metal electrode
IDT spacing
Piezoelectric substrate
wavelength
Pheromone mediated chemical communication in insects provides the key form of information exchange between individuals and the chemical cues often have associated behavioural changes via the neuroendocrine function. These semiochemicals are complex and diverse as most species rely upon a number of different compounds to convey specific information. This complex form of information exchange in invertebrates, mediated by chemicals, represents an unexplored form of communication and labelling technology that is yet to be exploited. The objective of our study was to:
Engineer biosynthetic components for chemical signal generation and detection based on insects’ pheromone production and sensing pathways.
Integrate these biosynthetic modules into a communication system.
Figure 2. Block diagram of the proposed engineering implementation of the Infochemical Communication System.
Figure 1. Biosynthetic modules forming an infochemical communication system. The chemoemitter exploits several subunits to produce infochemicals based on the enzymatic activity within the exocrine system of a moth and a microevaporator or a nebulizer (Q) releases the infochemical blend. The chemoreceiver exploits transmembrane domain (TD) olfactory receptors, which are transduced (T) using binding specific changes. Infochemical binding signals are processed in a ratiometric neuronal model based on the antennal lobe of the same animal.
For the chosen model biological system, each of these biological processes will be characterised and deployed in MEMS-based microreactors, novel biological microsensors, and artificial neuronal algorithms with VLSI implementation.
Figure 3. The basic principle of exciting surface acoustic waves by an interdigital transducer created by micro-patterned metal electrodes on a piezoelectric substrate (top). Schematic diagram of a SAW sensor consisting of input and output transducers( bottom).
A surface acoustic wave (SAW)-based sensor was developed that is functionalized with a biological layer and enables the detection of chemicals at very low concentrations. For the development of an olfactory receptor-based sensor for detecting pheromone signaling, a heterologous expression system, human embryonic kidney 293 (HEK293) cells, were employed because olfactory receptors can be efficiently expressed and then coupled to the artificial acousto-electric system for ligand detection.,
In SAW-based sensors, the input interdigital transducer (IDT) sets up an electric field in the substrate that by means of the piezoelectric effect generates a surface acoustic wave propagating towards the output IDT which in turn converts this wave into an electrical signal. Changes in the properties of the adjacent biological layer or liquid change the propagation characteristics of the wave (i.e. attenuation, phase, frequency), thus, allowing detection.
Theory of SAW sensors
Changes inside and on the cell membrane of the HEK293 cells induced by the ligand-receptor interaction are detected by surface acoustic waves that – depending on the frequency – penetrate into different regions of the cells, such as the nucleus, the cytoplasm and the bilipid layer.
Figure 5. (a) Optical microscope image of a dual delay line SAW sensor fabricated using Au/Cr electrodes and a LiTaO3 substrate. (b) Higher magnification image of the interdigitated transducer electrodes.
The SAW biosensors were designed in dual delay-line and dual resonator configuration to allow differential measurements in which only one device of the pair is coated with functionalized HEK293 cells expressing olfactory receptors while the other is coated with non-functionalized (i.e. wild type) HEK293 cells. Measuring the difference between the signals of the two delay-lines ameliorates environmental and other common mode variations and ensures that the measured responses are produced purely by the functionalized cells.
Cell growth and monitoring
a)
b)
Figure 4. Schematic ‘fried-egg’ representation of a human embryonic kidney 293 cell on a lithium tantalate surface acoustic wave device showing the different wave penetration depths required to monitor ligand binding-induced changes inside and on the surface of the cells
HEK293 attachment and viability on LiTaO3 and Au/Cr/LiTaO3 surfaces were confirmed by immobilizing HEK293 cells onto pre-sterilized SAW sensor chips. The cells were allowed to grow in an incubator environment for a period of 2 days and to confirm this the cell morphology on the sensors was examined under a scanning electron microscope via MTT cell viability assay. Both the electron micrographs and the MTT assay confirmed that HEK293 cells had grown on both metallised and unmetalized sensing areas on LiTaO3.
Figure 6. Scanning electron micrographs (increasing magnification, left to right) of HEK293 cells grown on a LiTaO3 SAW device with Au/Cr electrodes.
Power supply board
USB powered interface board
Oscillator board
SAW1
SAW2
Filter boards
A sensor interface circuitry for automated electro-acoustic HEK cell monitoring have been developed. The SAW sensors are placed in the feedback loop of an oscillator circuit that is connected to a laptop via an USB interface board that performs data processing as well.
Figure 8. Diagram of the sensor interface electronics consisting of a SAW sensor board and two filter boards mounted on the oscillator board, a power supply board and a main interface board.
Surface wave
AC
AC
Input transducer
Output transducer
Selective coating
Figure 9. Photograph of the SAW-based biosensor prototype.
USB powered interface board
Power supply board
SAW oscillator board with sensor
The prototype of the SAW-based sensor integrated with the interface circuitry is shown below:
Mixer
Amplifier
Low Pass Filter
Buffer
Low Pass Filter
SAW
Resonator
Low Pass Filter
Signal Converter
Micro-controller Interface
Sensing Oscillator (Immobilised)
Buffer
Temperature Control Unit
Temperature Control Unit
SAW
Resonator
Reference Oscillator
(Non-Immobilised)
1 0 1 0
Amplifier
Work towards integrating the SAW-based biosensors and the associated interface circuitry into a single monolithic analogue VLSI system have been started. The main components of this sensor implementation are shown below:
Figure 10. System diagram of aVLSI interfacing stage of individual sensing elements .
Figure 11. System diagram of aVLSI interfacing stage of individual sensing elements .
The physical layout of the initial aVLSI stage is shown below: