## Slide 1: Advantages and Disadvantages of CFD Methods
By Ahmed Al Makky

## Slide 2: As a Researcher what are you looking for?
1-Accuracy, e.g How accurate can it predict flow properties ?
2-Dose it work in confined or none confined boundary.
3-Can it calculate swirling flows.
4-Dose it use a lot of computer resources.
5-how many equations have to be solved for the problem.
6-can it describe circulation and separation.

## Slide 3
7-Can it be used to predict scalar transport properties.
8-Can it predict shear layer thickness (thin and thick).
9-has it been validated in the research and industrial sector and has that lead to the confidence of using it.
10-how many conditions initial , boundary ..(input parameters need to be supplied).

## Slide 4: Mixing Length Model
Advantages:
Easy to implement and cheap in terms
of computing resources.
Good predictions for thin shear layers: jets,
mixing layers, wakes and boundary layers.
Can be used to predict turbulent transport
of scalar quantities.

## Slide 5: Disadvantages:
Completely incapable of describing flows with separation and recirculation.
Only calculates mean flow properties and turbulent shear stress
The mixing length model is not used on its own in general purpose CFD, but we will find it embedded in more sophisticated turbulence models to describe near wall behaviour.

## Slide 6: Standard K-E model assessment
Advantages:
Simplest turbulence model for which only initial
and/ or boundary conditions need to be supplied.
Excellent performance for many industrial
relevant flows.
Well established, the most widely validated
turbulence model.
Performs well in confined flows where the
Reynolds Shear stresses are most important.

## Slide 7
More expensive to implement than mixing length model (two extra PDE).
Poor performance in a variety of important cases such as:
1-Some unconfined flows.
2-flows with large extra strains (Curved boundary layers, swirling flows).
3-Rotating Flows.
4-Flows driven by anisotropy of normal Reynolds stresses.
Disadvantages:

## Slide 8: Reynolds Stress Equation models(RSM):
Advantages:
Potentially the most general of all classical turbulence models
Only initial and /or boundary conditions need to be supplied
Very accurate calculation of mean flow properties and all Reynolds stresses for many simple and more complex flows including wall jets, asymmetric channel and non-circular duct flows and curved flows.

## Slide 9: Disadvantages:
Very large computing costs (Seven extra PDEs)
Not widely validated as the mixing length K-E models.
Performs just as poorly as the K-E model in some flows due to identical problems with the e-equation modelling (e.g. axis metric jets and unconfined recirculation flows)

## Slide 10: K-E models:
Wilcox k-w model
Menter SST k-w model

## Slide 11: Algebraic Stress Equation model
Advantages:
Cheap method to account for Reynolds stress anisotropy
Potentially combines the generality of approach of the RSM (good modelling of buoyancy and rotation effects possible) with the economy of the k-e model.
Successfully applied to isothermal and buoyant thin shear layers.

## Slide 12: Disadvantages:
Only slightly more expensive the K-E model (two PDE and a system of algebraic equations).
Not a widely validated as the mixing length and K-E models.
Some disadvantages as RSM apply.
Model is severely restricted in flows where the transport assumptions for convective and diffusive effects do not apply-Validation is necessary to define performance limits.

## Slide 13: Large Eddie Simulation (LES)
Advantages:
You have the advantage to choose what size of eddies you want in your simulation.
Takes less computer recourses than DNS.
Its now been used in commercial codes such as Fluent.
It can be implemented on complex geometry.
Its been used in the simulation of combustion process.

## Slide 14: Disadvantages :
I would like to hear your views about that.

## Slide 15: LES models:
Smagorinksy-Lilly SGS model
Higher-order SGS models
Advanced SGS models

## Slide 16: Direct Numerical Simulation DNS
Advantages:
The unsteady Navier-Stokes equations are solved on spatial grids that are sufficiently fine that they can resolve the kolmogrov length scales which energy dissipation takes place with time steps sufficiently small to resolve the period of the fastest fluctuations.

## Slide 17
Disadvantages:
The calculations are highly costly in terms of computing recourses.
The method is not used for industrial flow computations and is mostly concentrated in the research sector of science.