## Slide 1: The use of digestates as a nutrient source in fertigated strawberries Rob Lillywhite Warwick Crop Centre

## Slide 2: Introduction
Practical aspects:
  Environmental issues
  System assumptions
  Digestate storage
  Operational issues
  Cost benefit analysis:
    Value as fertilizer
Conclusions

## Slide 3: Environmental Issues
  The use of digestates requires a new approach and has the potential for environmental risk
  Pathogens, PTEs, stability & contaminants
  PAS110 and Quality Protocol – no waste management controls – a ‘passport’ to safe use
New leak proof storage required - uncontrolled releases to the environment might be a problem
Odours - health & neighbour/worker issues

## Slide 4: Assumptions
Dilution scenarios | High | Low
Digestate dilution factor | 50 | 20
Plant density | 8 /m2 | 12 /m2
Volume of feed /plant /season | 30 l | 30 l
Volume of feed /ha /season | 2400 m3 | 3600 m3
Volume of digestate (undiluted) /ha /season | 48 m3 | 180 m3

## Slide 5: Digestate Storage
Volume | Type | Cost /m3/year over 10 yr | 20 m3 upfront cost | 40m3 upfront cost
1 m3 | White 1000 Litre IBC container | £ 7 | £1400 | £2400
1 m3 | New IBC, timber pallet | £ 10 | £2000 | £4000
10 m3 | CT2200JA Tank | £ 12 | £2400 | £4800
19 m3 | V19000 | £ 13 | £2600 | £5200
36 m3 | Elliptical Concrete Tank | £ 15 | £3000 | £6000
72 m3 | Small AD storage unit | £ 24 | £4800 | £9600

## Slide 6: Operational Issues
  The use of digestates requires some changes to existing production practices
  Install (agitated) storage capacity
  Total solids content & existing fertigation equipment
  Adjusting digestate nutrient and pH levels
  Customer acceptability (not yet an issue but likely to become one)

## Slide 7: Cost benefit analysis
  Value as fertilizer
  Net cost savings
  Risk vs benefit

## Slide 8: Value as Fertilizer
 | Amount added per 100l |  | Cost /ha /season (8 plants /m2) | 
 | Diluted digestate | Control | Diluted digestate | Control
KNO3 | 36 g | 15 g | £ 806 | £ 249
Ca(NO3)2 |  | 24 g |  | £ 1,672
Mono-potassium phosphate | 21 g | - | £ 720 | -
1-1-3 NPK | - | 52 g |  | £ 345
(TEC SF + Mg) | Same amounts in both |  | - | -
Total |  |  | £ 1,527 | £ 2,266
Total Saving |  |  | £740 (-33%) | 

## Slide 9: Net cost savings
 | Cost /ha /season (min) | Cost /ha /season (max)
Fertiliser cost saving through the use of digestate | - £ 740 | - £ 740
Digestate transport cost | £ 185 | £ 480
Digestate storage cost | £ 33 | £ 108
Total savings | - £ 522 | - £ 152
Total fertiliser cost (conventional method) | £ 2,266 | £ 2,266
Percentage of total fertiliser cost saved | - 23 % | - 7%

## Slide 10: Summary - Risk vs benefit
Value of strawberries /ha /season | £43,000 – £99,000
Typical cost saving due to the use of digestate /ha /season | £152 - £522
Savings relative to value of fruit /ha /season | 0.15% - 1.2%
Risk of yield being affected by introducing a novel fertilizing system | >> 1.2% ?

## Slide 11
    Key questions:
      Can digestate be used in these applications?
      What are the constraints?
      Can these be overcome?
      Are there business benefits?
      Should the ADQP be changed?
WRAP Horticulture pre-feasibility trials
Notes: NOTE – these uses are not currently allowed under ADQP

## Slide 12: Conclusions
Amended digestates can successfully be used to supply the nutrients required by a fertigated strawberry crop
Fruit yield and quality yield are (mostly) maintained (under experimental conditions)
Small financial saving are possible but are unlikely to out-weigh potential risks (loss of yield and quality, inexperience, additional material handling)
Most viable where AD and protected production is integrated
Unknown (but predictable) issues surrounding customer acceptance of fruits grown using digestates

## Slide 13
Questions?