## Slide 1: Extracting Cone Beam CT (CBCT) Dose Volume Statistics and Radiomics Features to Predict Optimum Adaptation Point in Thoracic Radiotherapy
Claire Lesley Fletcher UHCW (Claire.fletcher@uhcw.nhs.uk)
Jane Rogers UHB, Jon Duffy UoW

## Slide 2
Radical lung RT in UK is usually 55Gy in 20#
Daily CBCT indicates changes during treatment, but not routinely used for oART
Identifying a suitable point for offline adaptation might provide a pragmatic alternative to oART
Similar work exists for longer fractionation schemes (e.g. 66Gy/33#)
Background

## Slide 3
162 patients treated with 55Gy in 20# radical radiotherapy between 2018-2023 at UHCW
  154 lung
  8 Oesophagus
Patient Statistics

## Slide 4
Daily CBCTs collected
Imported to RayStation
Adjusted for Intensity fluctuations
  Normalise to signal in a 5cc volume at centre of heart
  Correct for daily value of region receiving 0-5Gy planned dose
Method

## Slide 5
Corrected CBCTs deformably registered to plCT
OARs and GTV mapped to the CBCTs
OARs outlined on plCT
CBCT #20 and OARs mapped onto CBCT #20
Fusion between plCT and CBCT #20

## Slide 6
Planned dose distribution recalculated on daily CBCTs
Deformed to the planning CT
Planned dose on PlCT
Dose from CBCT #20 deformed back onto plCT
Dose calculated on CBCT #20

## Slide 7
Several statistics were extracted to investigate:
  Change throughout the treatment course
  A point at which final changes could be predicted
  Effect of adapting treatment
Statistics extracted for each treatment fraction:
  GTV
  Density (pixel intensity) change
  V5 and V20 (volume of lung receiving 5Gy / 20Gy)
  MLD (mean lung dose)
  EUD (Equivalent Uniform Dose) to lung
  Radiomics features

## Slide 8
Data gathered for:
  1 week, 2 weeks, 3 weeks, 1/3 treatment, 2/3 treatment
For DVH statistics fitted exponential / linear models
Compared predicted final values at each stage to predicted value found using all data
Predicting Final Changes
Chart: Days after start of treatment
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
all data | 17.0126 | 17.0822 | 16.9005 | 16.6959 | 16.9043 | 16.7871 | 17.0932 | 17.0556 | 17.3891 | 17.4708 | 17.5046 | 17.8028 | 17.4788 | 17.5159 | 17.8602 | 17.6268 | 17.6765
three weeks data | 17.0126 | 17.0822 | 16.9005 | 16.6959 | 16.9043 | 16.7871 | 17.0932 | 17.0556 | 17.3891 | 17.4708 | 17.5046 | 17.8028
two weeks data | 17.0126 | 17.0822 | 16.9005 | 16.6959 | 16.9043 | 16.7871 | 17.0932 | 17.0556
one week data | 17.0126 | 17.0822 | 16.9005 | 16.6959
Chart: Days after start of treatment
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
all data | 57.3407 | 56.8113 | 56.5746 | 52.0324 | 49.646 | 40.1802 | 40.8567 | 37.1337 | 43.7933 | 35.0512 | 31.677 | 32.8932 | 32.5849 | 33.0043 | 33.4365 | 30.5859 | 31.8475 | 32.115
three weeks data | 57.3407 | 56.8113 | 56.5746 | 52.0324 | 49.646 | 40.1802 | 40.8567 | 37.1337 | 43.7933 | 35.0512 | 31.677 | 32.8932 | 32.5849
two weeks data | 57.3407 | 56.8113 | 56.5746 | 52.0324 | 49.646 | 40.1802 | 40.8567 | 37.1337 | 43.7933 | 35.0512
one week data | 57.3407 | 56.8113 | 56.5746 | 52.0324 | 49.646

## Slide 9
Adapted method from Berkovic 2015
Calculated % change in DVH values (V5, V20, MLD, EUD) at different points
Assumed replanned at this point and % change reset to zero
Summed change for each fraction
Final summed change for adaptation was compared to original change
Finding Optimum Adaptation Point
Chart: Days from start of treatment
| 0 | 1 | 2 | 3 | 4 | 7 | 8 | 9 | 10 | 11 | 14 | 15 | 16 | 17 | 18 | 21 | 22 | 23 | 24 | 25
no adaption | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912 | 2.9596 | 3.3824 | 3.8052 | 4.228 | 4.6508 | 5.9192 | 6.342 | 6.7648 | 7.1876 | 7.6104 | 8.8788 | 9.3016 | 9.7244 | 10.1472 | 10.57
adapt after week 1 | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912 | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912 | 2.9596 | 3.3824 | 3.8052 | 4.228 | 4.6508 | 5.9192 | 6.342 | 6.7648 | 7.1876 | 7.6104
adapt after week 2 | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912 | 2.9596 | 3.3824 | 3.8052 | 4.228 | 4.6508 | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912 | 2.9596 | 3.3824 | 3.8052 | 4.228 | 4.6508
adapt after week 3 | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912 | 2.9596 | 3.3824 | 3.8052 | 4.228 | 4.6508 | 5.9192 | 6.342 | 6.7648 | 7.1876 | 7.6104 | 0 | 0.4228 | 0.8456 | 1.2684 | 1.6912

## Slide 10
Using the PyRadiomics python package 601 features extracted from each corrected CBCT for:
  GTV, PTV, lung-GTV and lung-PTV
Adopted method suggested by Van Timmeren et al. (2017)
Selected features which showed a change more than C for at least 10% of patients at different points during treatment
+1.96*SD
  SD is standard deviation of feature change for all patients between CBCT #2 and #1
Radiomics Feature Analysis

## Slide 11
80% of patients showed a reduction in GTV
  Average -10% at end of treatment , Projected -18% at 50 days
    Lower than: Berkovic 2015, Elsayad 2018, Jabbour 2015 -~40% reduction at 40-45d
    Similar to: Brink 2013 -20% at 50 days, Kwint 2020 -18.5% 24#
Average EUD change:
  lung-GTV 2% increase
  lung-PTV 2.6% increase
Average Pixel intensity change:
  GTV 17% increase
  lung-PTV, lung-GTV 0.1% decrease
    No real detectable change during treatment
Results

## Slide 12
Point at which final values of EUD, GTV and GTV pixel intensity change could be predicted was 2 weeks
Optimum Point to Predict Final Changes
Chart: Fractional change in Lung-GTV EUD predicted using all data
P=0.890
Chart: Fractional change in GTV pixel intensity predicted using all data
P=0.239
P=0.777

## Slide 13
To minimise increases to MLD, EUD, V5 and V20 the optimum adaptation point was 2 weeks
  Berkovic 2015 found optimal adaptation point at #15/25
Chart: Lung-PTV shrinking tumours
| #5 | #10 | #15
EUD | 0.6841 | 0.9282 | 0.7074
mld | 0.6005 | 0.8665 | 0.6737
V5 | 0.2091 | 0.3801 | 0.3143
V20 | 0.5935 | 0.8574 | 0.6698
Chart: Lung-GTV shrinking tumours
| #5 | #10 | #15
EUD | 0.5259 | 0.7354 | 0.5645
mld | 0.506 | 0.7479 | 0.5846
V5 | 0.1915 | 0.3489 | 0.2882
V20 | 0.3958 | 0.6318 | 0.5061
Optimum Adaptation Point

## Slide 14
Stable number of radiomics features showing a detectable change for >10% patients at week 2
Van Timmeren 2017 Found week 2 too early to find stable detectable feature changes for GTV for >10 patients
Chart: Number of radiomics features with change >C for >10% patients
| 1 | 4 | 8 | 11 | 16 | 18 | 25
GTV | 22 | 228 | 351 | 349 | 380 | 169 | 395
PTV | 19 | 244 | 336 | 365 | 384 | 367 | 373
lung - GTV | 12 | 60 | 57 | 79 | 118 | 100 | 117
lung - PTV | 12 | 68 | 57 | 75 | 112 | 90 | 117
Radiomics Feature Analysis

## Slide 15
An optimal point for data analysis and prediction for DVH statistics and radiomics feature extraction was found to be week 2 of the UK regime
Previous work that found week 3 optimal in longer treatment regimes (Berkovic 2015 for DVH statistics, Van Timmeren 2017 for extracting radiomics)
This information could be used for adaptation strategies when combined with treatment outcome data
Conclusion

## Slide 16
Thanks for Listening

## Slide 17
References
Van Timmeren J et al., Feature selection methodology for longitudinal cone-beam CT radiomics, Acta Oncologica, 2017, 56(11): p. 1537-1543
Berkovic, P., et al., Adaptive radiotherapy for locally advanced non-small cell lung cancer, can we predict when and for whom? Acta Oncol, 2015. 54(9): p. 1438-44.
Brink, C., et al., Locoregional control of non-small cell lung cancer in relation to automated early assessment of tumor regression on cone beam computed tomography. Int J Radiat Oncol Biol Phys, 2014. 89(4): p. 916-23.
Jabbour, S.K., et al., Reduction in Tumor Volume by Cone Beam Computed Tomography Predicts Overall Survival in Non-Small Cell Lung Cancer Treated With Chemoradiation Therapy. Int J Radiat Oncol Biol Phys, 2015. 92(3): p. 627–33.
Elsayad, K., et al., Is tumor volume reduction during radiotherapy prognostic relevant in patients with stage III non-small cell lung cancer? Journal of Cancer Research and Clinical Oncology, 2018. 144(6): p. 1165–1171.
Kwint, M., et al., The prognostic value of volumetric changes of the primary tumor measured on Cone Beam-CT during radiotherapy for concurrent chemoradiation in NSCLC patients. Radiotherapy and Oncology, 2020. 146: p. 44–51.