## Slide 1: Using Hough Transform to reconstruct particle tracks in hptpc
Veera Mikola

## Slide 2: Reminder of randomised Hough Transform
Voxelize files using trex
Run through event(s) wanted
Create a dictionary consisting of all the coordinates and energy deposits in the event
Choose two points randomly from this dictionary and draw a line between them
From the line define and , and draw a 2-D histogram of the accumulator
Find peaks from the histogram using TSpectrum
Collect hits using the peak information
Find a start and an end point of the track

## Slide 3: Progress
Program finds the peaks
Program collects the hits, and from that defines the start and end points of the tracks
For events with multiple peaks found, have found two ways to exclude the tracks caused by “ghost peaks” (incorrect peaks usually found around the main peaks, mostly in short track/high noise events)
  Fake tracks, i.e. tracks that have a very low hit density (number of hits/distance of the track)
  Duplicate tracks, caused by peaks very close to each other. Look at the values of b and m for the tracks to cut these out

## Slide 4: Protons tracks

## Slide 5: Proton tracks

## Slide 6: The algorithm of finding the start and end point
Calculate the length of the line formed by the hits collected
Divide the line into 100 equal segments
Calculate the number of hits in each length segment and put it into a histogram
Define start and end points as being 10% of maximum in the histogram

## Slide 7: Proton tracks

## Slide 8: Proton tracks

## Slide 9: Proton tracks
Event5

## Slide 10: Proton tracks

## Slide 11: Multiplicity (number of tracks found)

## Slide 12: Fake tracks and duplicate tracks
Fake tracks
  Find the hit density of all tracks
  For tracks that have density less than 0.02 (found the limit looking at hit densities of events where more than 1 peak found) set the start and end point to 0
Duplicate tracks
  Look for the values for b and m (y-intercept and gradient) of the track
  If they are close to each other (limits found looking at events with more than 1 peaks) set start point and end point to 0
Currently for some rare tracks all tracks are cut off, but this is a work in progress

## Slide 13: Multiplicity after removing tracks (protons)
Fake track
Duplicate tracks

## Slide 14: Pion tracks

## Slide 15: Pion tracks

## Slide 16: Pion tracks

## Slide 17: Pion tracks

## Slide 18: Pion tracks
Event2

## Slide 19: Multiplicity (pions, 8 events)

## Slide 20: Multiplicity after removing tracks (pions)
Fake tracks
Duplicate trakcs

## Slide 21: Next…
Improve the detection of fake tracks and duplicate tracks
Try a different approach to finding the peaks (maybe try something else than TSpecturm?)
Test the programme using actual data from hptpc when possible