## Slide 1: Electron Paramagnetic Resonance CH921
Gavin W Morley,
Department of Physics,
University of Warwick

## Slide 2
Overview
Electron paramagnetic resonance
  What it is
  Why it’s useful

## Slide 3
Overview
Electron paramagnetic resonance
  What it is
  Why it’s useful
What does an EPR spectrum look like?
What is the resonant frequency for EPR?
Which things have an EPR signal?

## Slide 4
Overview
Electron paramagnetic resonance
  What it is
  …NMR for electrons

## Slide 5
Electron paramagnetic resonance (EPR)
… or electron spin resonance (ESR)
… or electron magnetic resonance (EMR)
… or ferromagnetic resonance (FMR)

## Slide 6
Magnetism
Electron spins tend to:
Paramagnetism: follow
Diamagnetism: oppose
Ferromagnetism: ignore
…an applied magnetic field

## Slide 7
From Steven Brown’s NMR lecture:

## Slide 8
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Photon energy
Magnetic field
An isolated spin I = ½ has m = ±½
m = +½
m = -½

## Slide 9
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Photon energy
Magnetic field
m = +½
m = -½

## Slide 10
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Magnetic field
Photon energy
Magnetic field
Photons reflected
m = +½
m = -½

## Slide 11
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Magnetic field
Photon energy
Magnetic field
Photons reflected
m = +½
m = -½

## Slide 12
Magnetic resonance
Isidor Isaac Rabi (1898 – 1988)
Energy of a spin ½
Magnetic field
Photon energy
Magnetic field
Photons reflected
m = +½
m = -½

## Slide 13
Magnetic resonance
Energy of a spin S = ½
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz
g is the EPR equivalent of chemical shielding in NMR,
µB is the Bohr magneton
Pieter Zeeman (1865 - 1943)
Notes: Zeeman effect

## Slide 14
Magnetic resonance condition
Energy of a spin S = ½
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz = hvres
= ħωres
Notes: Zeeman effect

## Slide 15
Magnetic field, Bz
Photons reflected
Electron paramagnetic resonance
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Bruker
fres = 10 GHz
fres = 240 GHz

## Slide 16
Electron paramagnetic resonance
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz
Notes: mu_N is the nuclear magneton and it is ~1000 times smaller than mu_B

## Slide 17
Electron paramagnetic resonance
Energy of a spin system
Magnetic field, Bz
Magnetic field, Bz
Photons reflected
Energy gap |ΔE| = g μB Bz
S = ½
ms = ±½
I = ½
mI = ±½ (= m)

## Slide 18
Energy of a spin system
Magnetic field, Bz
Photons reflected
A
mI = ½ mI = -½
Magnetic field, Bz
Electron paramagnetic resonance
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz ± A/2
A is the HYPERFINE COUPLING

## Slide 19
Photons reflected
A
Magnetic field, Bz
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
Stable free radicals:
BDPA
Nitroxides
DPPH
mI = ½ mI = -½

## Slide 20
Photons absorbed
A
Magnetic field, Bz
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
mI = ½ mI = -½

## Slide 21
Photons absorbed
A
Magnetic field, Bz
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
mI = 1 mI = 0 mI = -1

## Slide 22
Magnetic field, B
Electron paramagnetic resonance
Magnetic field modulation
(~10 to 100 kHz)
Advantage: noise only at
modulation frequency
Photons absorbed
Differential
absorption
mI = 1 mI = 0 mI = -1

## Slide 23
Differentialabsorption
Magnetic field, B
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
A
mI = 1 mI = 0 mI = -1

## Slide 24
Differentialabsorption
Magnetic field, B
TEMPO
£20/g from Aldrich
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
Electron paramagnetic resonance
mI = 1 mI = 0 mI = -1

## Slide 25
Electron paramagnetic resonance
spectrometer
Console
Computer
Electromagnet (up to 1.5 T) or superconducting magnet for higher field
S
Microwave bridge

## Slide 26
Electron paramagnetic resonance
spectrometer
S
Bridge
source
detector
Microwave resonator
Modulation coils

## Slide 27
Electron paramagnetic resonance
spectrometer
S
Bridge
source
detector
Microwave resonator
Modulation coils

## Slide 28
Electron paramagnetic resonance
spectrometer
S
Bridge
source
detector
Microwave resonator
Modulation coils

## Slide 29
Electron paramagnetic resonance
spectrometer
CW EPR so far…
Pulsed EPR next

## Slide 30
Pulsed electron paramagnetic resonance spectrometer
S
Bridge
High power pulsed source
Protected detector
Microwave resonator
Modulation coils off

## Slide 31
Pulsed electron paramagnetic resonance

## Slide 32
Pulsed electron paramagnetic resonance
Bres
resonance condition g mB Bres = h f
f
p/2
Free induction decay (FID) on timescale T2*
Polarize (thermalize) on timescale T1

## Slide 33
Pulsed EPR
f
p/2
J van Tol, L-C Brunel & RJ Wylde, Rev Sci Instrum 76, 076101 (2005)
~100 MHz width
Pulse width < 500 MHz
Resonator ringing  deadtime
Short T2 and T2* compared to NMR
Homogeneous (T2) can be much longer than inhomogeneous (T2*) so most pulsed EPR uses spin echo

## Slide 34: The rotating frame of reference
Larmor precession

## Slide 35: The rotating frame of reference
Larmor precession

## Slide 36: The rotating frame of reference
Larmor precession

## Slide 37
Rotating frame

## Slide 38
Spin echo
In rotating frame

## Slide 39
Spin echo
In rotating frame

## Slide 40
Spin echo decay
Erwin L Hahn (1921-2016) Photo: AIP Emilio Segre Visual Archives, Stephen Jacobs Collection

## Slide 41
Spin echo decay
Erwin L Hahn (1921-2016) Photo: AIP Emilio Segre Visual Archives, Stephen Jacobs Collection
Notes: Hahn echo

## Slide 42
Pulsed EPR
Double electron-electron resonance (DEER) allows distances between two electron spins in the range 2 to 6 nm to be measured (cf < 1 nm by NMR for two nuclear spins)
Dipolar coupling α 1/r3
Site directed spin labelling with
one or more TEMPO

## Slide 43
Energy of a spin system
Magnetic field, Bz
Photons reflected
A
Magnetic field, Bz
Electron nuclear double resonance (ENDOR)
mI = ½ mI = -½
S = ½
ms = ±½
I = ½
mI = ±½ (= m)
Energy gap |ΔE| = g μB Bz ± A/2

## Slide 44
Electron nuclear double resonance (ENDOR)
Why do ENDOR instead of NMR?
only need ~1010 spins instead of ~1015
NMR may be difficult near the electron spin
Energy of a spin system
Magnetic field, Bz
Energy gap |ΔE| = g μB Bz ± A/2

## Slide 45
Electron nuclear double resonance (ENDOR)
B0 is static magnetic field
B1 is EPR magnetic field
B2 is NMR magnetic field
Energy of a spin system
Magnetic field, B0
Energy gap |ΔE| = g μB B0 ± A/2

## Slide 46
ENDOR for quantum computing
Classical Quantum
computer computer
Bits Qubits
0 or 1 α 0 + β 1
Notes: A normal computer stores information as bits that can be 1 or 0. A quantum computer uses qubits: two level quantum systems such as spins 1/2

## Slide 47
Spin qubits in diamond

## Slide 48
Conclusions
  EPR Applications:
  Studying biomolecules
  Quality control in beer, wine etc
  Radiation dose received by teeth
What does an EPR spectrum look like?
What is the resonant frequency for EPR?
Which things have an EPR signal?