## Slide 1: Our Demand Driven Journey
Brian Dooley

## Slide 2: Agenda
The case for change
Our approach
Where are we now
Takeaways and myth busters

## Slide 3: The Case for Change
Chart: FC Error SKU Mix
| 42248 | 42278 | 42309 | 42339 | 42370 | 42401 | 42430 | 42461 | 42491 | 42522 | 42552 | 42583 | 42614 | 42644 | 42675
SKUS <20% Err | 0.2906 | 0.17094 | 0.12821 | 0.17094 | 0.18803 | 0.22222 | 0.25641 | 0.22222 | 0.2735 | 0.26496 | 0.23077 | 0.18803 | 0.24786 | 0.25641 | 0.24786
SKUS 20%-50% Err | 0.2906 | 0.22222 | 0.22222 | 0.33333 | 0.2735 | 0.33333 | 0.23932 | 0.21368 | 0.24786 | 0.28205 | 0.23932 | 0.32479 | 0.23077 | 0.21368 | 0.25641
SKUS > 50% Err | 0.4188 | 0.60684 | 0.64957 | 0.49573 | 0.53846 | 0.44444 | 0.50427 | 0.5641 | 0.47863 | 0.45299 | 0.52991 | 0.48718 | 0.52137 | 0.52991 | 0.49573
Problem statement: Our forecasts are not accurate enough
SKU level forecast accuracy is destroying flow:
  Schedule break ins
  Expedites
  Stock outs and over stocks
Clearly the solution is obvious
Improve forecast accuracy
“If I had asked people what they wanted, they would have said faster horses”
Henry Ford
Or are we solving the wrong problem

## Slide 4: DDMRP - Testing the theory with a simulation
Chart: Actual Inventory Evolution
Chart: Actual vs DDMRP Simulation – 6 month Inventory Evolution
Simulation model built using 6 months history of actual daily orders
Two groups of SKUs from the same family modelled that had been historically over and under forecast but at the aggregate level had excellent accuracy
RESULTS
Stock is in balance and total inventory is halved
NOT Dependant on Forecast so decoupled from forecast error
NO Service issues
LESS Inventory
STABLE load on factory
NO costs of failure
Manufacturing Lead Time

## Slide 5: Where are we now - End to End Demand Driven Planning
DDMRP
daily
DDS&OP
weekly/monthly
Adaptive S&OP
quarterly
Actual Demand
Strategy Technology
Orchestr8 configuration
& Parameter settings
Variance analysis
Forward projections
Simulation & what-if
Agreed operating envelope to support business plan
Demand forecasts

## Slide 6: Key Takeaways & Myth Busters
Demand Driven has and is delivering
Supply chain ‘de-risked’ from forecast accuracy
Strong positive impact on cash flow and ROCE
Maintained or improved service levels
Significant inventory reduction
Release of supply chain capacity by not producing, buying and storing the wrong stuff
Cost reduction – lower planning effort with improved outcomes – lower expedite costs
Myth Busters
Demand driven is not just DDMRP
It’s not about choosing between forecasting or DDMRP
Equally it does not been better forecasting (or more expensive forecasting tools)
Don’t assume because of it’s elegant simplicity it’s easy to implement – the change management challenge is significant

## Slide 7: Supplemental Material

## Slide 8: A bit about us

## Slide 9: Enabling Demand Driven
Red
Base
Red Safety
Yellow
Green
Determines supply order generation frequency & size, is the larger of:
MOQ
Desired order cycle
ADU x Lead Time x Lead Time factor
The heart of the demand coverage in the buffer
Always sized as 100% ADU x Lead Time
The embedded safety in the buffer
Red zone base established based on lead time factor = ADU x Lead Time x Lead Time factor
Red zone safety is determined by variability factor = Red zone base x variability factor
On Hand Stock
Open Purchase Orders
Open Customer Orders
Net Flow
Net Flow = On Hand + Open PO’s
– Open Customer Orders
Triggering a Purchase Order
When net flow drops out of the green zone a PO is placed to take the net flow position back to the top of green
DDMRP
Supply
Demand
Putting the supply chain capability in place to respond and adapt to ACTUAL customer demand

## Slide 10: Strategic Inventory Buffer Positioning
Cables Factory
Supplier
Supplier
Supplier
NDC
NDC
FSL
FSL
FSL
Supplier
C
Customer
Customer
Customer
C
Customer
Customer
Customer
FSL = Forward Stock Location (96)
Over 125,000 individual Item:Location combinations

## Slide 11: Planning vs Execution or Net Flow vs On Hand
Red
Base
Red Safety
Yellow
Green
Red
Yellow
Green
Net flow zones
On Hand Alert Zones
Net flow
On hand
Net flow
On hand
Net flow
On hand
Part1
Part2
Part3
Part | Planning Action | Execution Action
PART1 | No Action | No Action
PART2 | Place New PO | No Action
PART3 | No Action | Expedite Open PO’s

## Slide 12: DDMRP Excel model – clear plan priorities
Index | BT IC | Desc | ADU | MOQ | Order Cycle (days) | + On Order | -Qualified Sales Orders | On Hand | =Available Stock | Recommended Order | 
1 | Part1 |  | 601.08 | 8100 | 15 | 32,400 | 4,000 | 6,169 | 34,569 | 8100 | 
2 | Part2 |  | 58.69 | 6000 | 102 | 6,000 | 0 | 631 | 6,631 | 0 | 
3 | Part3 |  | 938.25 | 5030 | 15 | 45,270 | 0 | 10,542 | 55,812 | 15090 | 
4 | Part4 |  | 3417.14 | 8100 | 15 | 146,853 | 1,950 | 48,043 | 192,946 | 64800 | 
5 | Part5 |  | 347.85 | 8075 | 23 | 25,089 | 0 | 5,092 | 30,181 | 0 | 
6 | Part6 |  | 213.46 | 4840 | 23 | 10,502 | 1,500 | 4,491 | 13,493 | 0 | 
7 | Part7 |  | 8.63 | 12 | 15 | 415 | 13 | 194 | 596 | 0 | 
8 | Part8 |  | 2569.15 | 10100 | 15 | 125,193 | 2,500 | 67,041 | 189,734 | 0 | 
9 | Part9 |  | 190.77 | 10000 | 52 | 10,400 | 0 | 5,200 | 15,600 | 0 | 
10 | Part10 |  | 1670.35 | 4015 | 15 | 70,506 | 3,975 | 50,872 | 117,403 | 0 | 
11 | Part11 |  | 156.08 | 8100 | 52 | 8,100 | 790 | 4,951 | 12,261 | 0 | 
12 | Part12 |  | 6.66 | 50 | 15 | 250 | 10 | 221 | 461 | 0 | 
13 | Part13 |  | 711.98 | 3040 | 15 | 14,310 | 1,940 | 24,728 | 37,098 | 15200 | 
14 | Part14 |  | 10310.63 | 14050 | 15 | 315,961 | 13,635 | 360,075 | 662,401 | 0 | 
Critical Items
Expedite existing POs
Call out any delays
On Hand / ADU = Days of cover
Potentially at risk items
Monitor
Check days of cover vs PO due date
Call out any delays
BT IC | Desc | On Hand | ADU | OH Cover | PO NUMBER | PO DATE | QUANTITY ORDERED | QUANTITY DELIVERED | NEED BY DATE
Part1 |  | 6,169 | 601 | 10 | xxxxxxxxxxx | 25/05/2016 | 8100 | 0 | 30/06/2016
 |  |  |  |  | xxxxxxxxxxx | 29/06/2016 | 16200 | 0 | 31/07/2016
 |  |  |  |  | xxxxxxxxxxx | 13/05/2016 | 8100 | 0 | 27/06/2016
Part2 |  | 631 | 59 | 11 | xxxxxxxxxxx | 07/06/2016 | 6000 | 0 | 19/07/2016
Part3 |  | 10,542 | 938 | 11 | xxxxxxxxxxx | 05/07/2016 | 15090 | 0 | 16/08/2016
 |  |  |  |  | xxxxxxxxxxx | 17/06/2016 | 15090 | 0 | 29/07/2016
 |  |  |  |  | xxxxxxxxxxx | 29/06/2016 | 10060 | 0 | 31/07/2016
 |  |  |  |  | xxxxxxxxxxx | 29/06/2016 | 5030 | 0 | 15/08/2016
Part4 |  | 48,043 | 3,417 | 14 | xxxxxxxxxxx | 07/06/2016 | 72900 | 7047 | 19/07/2016
 |  |  |  |  | xxxxxxxxxxx | 29/06/2016 | 48600 | 0 | 31/07/2016
 |  |  |  |  | xxxxxxxxxxx | 29/06/2016 | 32400 | 0 | 15/08/2016
Part5 |  | 5,092 | 348 | 15 | xxxxxxxxxxx | 13/05/2016 | 8075 | 7211 | 27/06/2016
 |  |  |  |  | xxxxxxxxxxx | 17/06/2016 | 8075 | 0 | 29/07/2016
 |  |  |  |  | xxxxxxxxxxx | 05/07/2016 | 16150 | 0 | 16/08/2016
Expedite
Confirm delivery date

## Slide 13: Developing DDS&OP
Vision was to review buffers monthly with finance and operations with signoff of buffers the governance & control for PO placement
Too many buffers and external stakeholders unsure of what or how to signoff
Chart: Aggregate Buffer Evolution
| Starting Buffers | Mar-17 | Apr-17 | May-17
Red Zone (£) | 9018861.1968 | 8802822.9069 | 6013138.9468 | 8515053.32
Yellow Zone (£) | 29210022.7776 | 27004978.4953 | 27187512.612 | 31011705.61
Green Zone (£) | 20980014.1755 | 14053825.5978 | 14448922.9334 | 14838772.44
MOQs addressed
Master data integrity – lead times updated
Outliers excluded from variability
Lead time variability added in
New ADU rule between forecast and actual
Monthly DDS&OP to set policies for the DDOM and review the high level impact along with any significant changes
Weekly DDS&OP Tactical adjustments to the DDOM within the agreed policies
Weekly DDS&OP Tactical adjustments to the DDOM within the agreed policies
Weekly DDS&OP Tactical adjustments to the DDOM within the agreed policies
Weekly DDS&OP Tactical adjustments to the DDOM within the agreed policies
Monthly DDS&OP Policy Setting for the DDOM