## Slide 1: Warwick EM Facilities
Peng Wang
Electron Microscopy Research Technical Platform (EM-RTP)
Department of Physics
University of Warwick

## Slide 2: Warwick Research Technology Platforms

## Slide 3: Warwick Electron Microscopy Facilities
Electron Microscopy Research Technology Platform
Key Contact: Steve York
Email: s.j.york@warwick.ac.uk
Telephone: +44 (0)2476 523391
Website: https://warwick.ac.uk/research/rtp/em/
Advanced Bioimaging Research Technology Platform
Key Contact: Dr Saskia Bakker
Email: s.bakker@warwick.ac.uk
Telephone: +44 (0)2476 574095
Website: https://warwick.ac.uk/research/rtp/bioimaging/whatwecando/
WMG Electron Microscopy Suite
Key Contact: Geoff West
Email: g.west@warwick.ac.uk
Facility Email: wmgbusiness@warwick.ac.uk
Telephone: +44 (0)2476 573501
Website: https://warwick.ac.uk/fac/sci/wmg/research/research-areas/steels/facilities-and-equipment/
National Electron Diffraction Facility (Warwick)
Key Contact: David Walker
Email: d.walker.2@warwick.ac.uk
Facility Email: info@ncs.ac.uk
Telephone: +44 (0)24 76151299
Website: https://warwick.ac.uk/research/rtp/xrd/electrondiffraction/
Electron Microscopy Research Technology Platform
Peng Wang, Steve York
Advanced Bioimaging Research Technology Platform
Corinne Smith, Saskia Bakker
WMG Electron Microscopy Suite
Geoff West
National Electron Diffraction Facility (Warwick)
David Walker, Jere Tidey
Aberration Corrected S/TEM
Electron diffractometer
S/TEM
EELS Spectroscopy
SEM and FIB
Cryo-SEM, volume electron microscopy
Cryo-EM,single-particle samples and tomography
pFIB
SEM
3D microcrystal ED

## Slide 4: Warwick EM Research Technique Platform (RTP)
DENS
Double-tilt Heating Holder
Gatan
N2 Cryo-EM Holder
Nova
Electrochemistry Holder
Protochip
Liquid Holder
4D-STEM Detector
Merlin (MediPix)
Notes: Over the last decade the EM-RTP has grown into one of the UK’s largest, most active and successful centres for electron microscopy, with an investment of over £10 million in state-of-the-art instrumentation, supporting research on grants and commercial funding that exceeds £30 million.

## Slide 5: Warwick Microscopy Group
Academics
Peng Wang
Richard Beanland
Ana Sanchez
Alex Robertson
Jeremy Sloan
Neil Wilson
Technical Staff
Peng Wang (Academic Director )
Steve York (Facility Manager)
Steve Hindmarsh, Yisong Han, Andrew Unsworth
Notes: As a result, Warwick hosts a critical mass of expertise in this field, currently comprising 5 world-leading academics working in electron microscopy, a user community of over 200 researchers across over 40 research groups at Warwick, and over 50 external academic and industrial partners.

## Slide 6: Research Interests of the EM Group
AC-STEM
Spectroscopy
Diffraction and Crystallography
High Resolution STEM Imaging
‘In-operando’ and ‘In-situ’ EM
Electron Energy Loss Spectroscopy
Crystallography and Diffractive Imaging
Functional Materials
Pixelated Detector
Geen and Energy Materials
Notes: Basing upon Aberration corrected STEM, I have research area.
Using conventional 2D imaging and EELS, we are looking the free standing 2D oxide thin film and their ferrielectric properties at atomic level.
Using home-made in situ platform and FIB fabrication we are looking at Nano-device’s switching dynamics.
We are aslo working on technique development, such as 3D and 4D STEM
As 4D STEM is an emergent and frontier characterization, which more interested to Warwick’s, as new utrastfast is coming, I wil present it to today.

## Slide 7: About Myself
2003-2006 PhD, SuperSTEM Electron Microscopy National Lab &University of Liverpool, UK
2006-2007 Research Associate, SuperSTEM Electron Microscopy National Lab
2008-2012 Research Fellow, University of Oxford, Electron Microscopy Group.
2012-2021, Professor, Nanjing University, China
  Developed a sub-angstrom EM facility
2021-now, Associate Professor, University of Warwick, UK
2025-now, Director of EM-RTP
https://pengwang.org
Notes: Before diving deeper, let me share my journey. From PhD work at Liverpool to leading the Nanjing EM facility, I’ve seen firsthand how TEM evolves. At Warwick, we’re pushing boundaries with sub-ångström resolution—imaging atoms as small as 0.1 nanometers. This course will draw from these experiences to prepare you for cutting-edge research.

## Slide 8: My Research Background
2003-2007
SuperSTEM
2007-2008
SuperSTEM
2008-2012
Oxford
2012-2021
Nanjing
2021-Now Warwick
UK National SuperSTEM Laboratory
Oxford EM Centre
Nanjing EM Centre
3rd order corrected VG-STEM
5th order NION
  JEOL MCO 2200
  Titan3 Cubed 60-300
Warwick EM RTP
  ARM JEOL 200F
Notes: My research has been carried out in key electron microscopy groups or facilities working with state-of-the-art microscopes.

## Slide 9: Research Interests of My Group
Aberration Corrected STEM
In situ
TEM
2D Imaging & EELS
4D-STEM
3D Imaging
Ptychographic Imaging
Pixelated Detector
Nature Comm., 11, 2773 (2020).
Advanced Mater., e1903747 (2019).
Phys. Rev. Lett., 121, 146101 (2018).
Nature Comm., 8, 163 (2017).
Three Dimensional Imaging
Titled Tomography
Nature Comm., 12, 3011, (2021)
Phys. Rev. Lett., 104, 200801 (2010)
Nature Nanotechnology 3, 168 (2008)
Confocal EM
2D Materials and Interfaces
Free Standing 2D Oxide
(Flexoelectricity)
Nature, 570, 87 (2019).
Nature Communications 10, 5589, (2019)
Nature Nanotechnology 3, 676, (2008)
Nature Electronics, 2, 563 (2019)
Ultramicroscopy, 194, 57 (2018).
Nature Electronics, 1, 130 (2018)
Nano-device Switching
Domain
wall
Notes: Basing upon Aberration corrected STEM, I have research area.
Using conventional 2D imaging and EELS, we are looking the free standing 2D oxide thin film and their ferrielectric properties at atomic level.
Using home-made in situ platform and FIB fabrication we are looking at Nano-device’s switching dynamics.
We are aslo working on technique development, such as 3D and 4D STEM
As 4D STEM is an emergent and frontier characterization, which more interested to Warwick’s, as new utrastfast is coming, I am working on nowadays.
For instance, our work on graphene (*Nature Communications*, 2019) revealed how atomic defects influence conductivity. Such insights are only possible with advanced TEM techniques."

## Slide 10: What is 4D STEM?
Big 4D Dataset
Reconstruction Algorithm
Computational Reconstructed Image
Applied Physics Letters 113.3 (2018): 033104.
Notes: What should we do in the future. We propose to use a 2D ultrafast pixelatted detectro to replace all the current detector. At each scanning position, we can acquire a two image of the DP. After we scan 2D array of the positions, a 4D dataset si formed. Then we will use computer algorithm to reconstruct the image.

## Slide 11: 4D-STEM and Ptychography (2007-2017)
HAADF
HAADF
Phase
CeO2 : Ce (58), O(8)
FFT
Atomic Resolution
P. Wang* et al., Sci Rep 7, 2857 (2017)
P. Wang*, et al., Nature Comm, 8, 163 (2017).
Nanjing University
Ronchigram detector (1k x 1k)
Krivanek Ultramicroscopy 2007
Ronchigram or Far-field DP
SuperSTEM II @ SuperSTEM Lab
Ptychographic Phase
Earlier Trials in 2007

## Slide 12: 4D-STEM and Ptychography (2017-)
a
VP6
b
VP6
100 nm
50 nm
L. Zhou,.. C.S. Allen, ..& P. Wang*. Nature Comms, 11, 2773 (2020)
Cryogenic Ptychography for Bio
J. Song, C. S. Allen, .., P. Wang* & et al,
Scientific Reports, 9, 3919 (2019)
Detectors
HAADF
HAADF
Focused-type STEM
diffraction pattern
CCD
Defocused Ptychography
Dose: 2x103 e/Å2
Dose: 2x103e/Å2
MoS2
Low-dose Ptychography
ePSIC Diamond
key specifications:
1-bit (18800 fps);
6-bit (3200 fps);
12-bit (1600 fps);
MerlinEM

## Slide 13: New 4D-STEM Capabilities at Warwick
Merlin (MediPix)
  JEOL 2100
STEMx+Oneview
  ARM JEOL 200-80kV

## Slide 14
Ptychography
DPC Imaging
Strain Mapping
Visual Imaging
PACBED
Local Symmetry Mapping
Orientation Mapping
AI
Ultramicroscopy, 2013, 124: 71-76.
Chem. Mater. 2011, 23, 20, 4515
Ultramicroscopy 110, 118 (2010)
Nature Physics 8, 611-615, (2012).
Adv. Struct. Chem. Imag. 4:10 (2018)
Nature Communications, 8, 163 (2017).
4D-STEM

## Slide 15: Access to Our Facility
9.30 | Coffee and Arrival (room PS1.28) | 
10.00 | Welcome and introduction | Dr Yisong Han
 | Keynote: Electron Microscopy at EM RTP and Warwick | Prof Peng Wang (Director of EM RTP and Physics)
 | Linking Structure to Performance Across Scales: Multiscale Insights with FIB-SEM | Dr Martin Slama (Tescan)
 | In situ TEM for understanding rechargeable batteries | Prof Alex Robertson (Physics)
 | Accessing conventional synthetic polymers at the atomic level | Dr Evelina Liarou (Chemistry)
 | Is STEM in SEM a viable alternative to TEM? | Dr. Patrick Trimby (Zeiss)
 | Mapping electric fields of in-operando devices in the electron microscope | Dr Eoin Moynihan (Physics)
 | 4D‑STEM Unveiled: Capturing Diffraction at Every Pixel | Dr Saleh Gorji (Gatan)
 | Structure–Property Studies of Nanoscale Materials Using Precession Electron Diffraction in TEM | Dr Thanos Galanis (NanoMEGAS)
12.00 | Networking lunch (room MAS2.05/2.06) | 
13.00 | Lab tours | 
13.30 | Demonstration 1: STEMx and 4D-STEM | Gatan
 | Demonstration 2: Focused Ion Beam | Tescan
 | Demonstration 3: STEM in SEM using a quadrant detector | Zeiss
 | Demonstration 4: JEOL ARM200f TEM | Warwick staff
EM-RTP
Peng Wang, Director
Peng.wang.3@warwick.ac.uk
Steve York, Facility Manager
S.J.York@warwick.ac.uk
Yisong Han, Scientific Officer (4D-STEM)
Yisong.Han@warwick.ac.uk
Warwick Scientific Services
Claire Gerard
Warwick Scientific Services Manager
Millburn House, University of Warwick
Tel: +447385 145064 Email: c.gerard@warwick.ac.uk