## Slide 1
INTRODUCTION
Solvents play a major role in chemical process . Catalyst solubility, yield and stereo selectivity all vary from solvent to solvent.1, 3 Proper solvent selection leads to great benefits, such as reduction of cost and emission.
Olefin metathesis has become one of the most powerful tools for the formation of carbon – carbon double bonds. Ring closing metathesis (RCM) is one of the different variations of olefin metathesis, it is simply an intermolecular olefin metathesis reaction giving rise to a cyclo alkene as a major product and an acyclic alkene. This project involved the study of the RCM of dienes.
In this project, focus was shifted to solvents with little or no impact on the environment. These solvents are biodegradable, have reduced ozone depletion, and are produced from renewable resources.
2. METHOD
A list of solvent functional groups was put together by Folić et al..4 Using computer aided molecular design, these can be used as building blocks for designing new solvent for chemical reactions
In this project, non biodegradable functional groups that may cause harm to both humans and the environment were eliminated . The list of functional groups that are considered to be of less or no harm to the environment include: CCH3, CCH2, CCH, CH=CH, CH2= C, CH=C, CH2=CH, CH=C, C=C, CH, CCH3, CCH2 , CCH, OH, CH2COO, CH3CO, CH2CO, CH3COO, CHO, CH3O, CH2O, CH-O, CH2NH2, CH3N, CH3NH, CH2N, CH2NH, CNH2 and COOH.
RCM of diethyl diallylmalonate(1) and N-allyl-N (2- methyl -2- propenyl)- p - toluene sulfonamide(2) using 1,3- dimesityl- 4,5- di hydroimidazol -2- ylidene (Grubbs II) as a catalyst was done in the readily available eco friendly solvents.
Substrate | Product | Solvent | Yield [%] | Time / h
3. RESULTS
Table 1. Grubbs (II) catalysed ring closing metathesis dienes
Dimethyl carbonate | 99 | 5.5
Diethyl ether | 69 | 4.5
Methanol | 10 | 24
Ethanol | 5 | 24
Dimethyl carbonate | 86 | 24
Diethyl ether | 51 | 24
Methanol | - | 24
Ethanol | - | 24
5. Future work
Kinetic study of RCM reaction in dimethyl carbonate and diethyl ether
Further study regarding the effect of the above functional groups on the environment .
Acknowledgment
I would like to thank Dr, Paul Taylor for giving me the opportunity to get involved in this project and for all the support and guidance that he has offered throughout . Special thanks to Justine Renaud, Kate Casey- Green, David Guajiro, Phil Rushworth and Sophie Royall.
References
M. S. Sanford, J.A. Love and R.H. Grubbs , J . Am. Chem. Soc. 2001, 123, 6543
C.S. Adjiman, A. J. Clarke, G. Cooper and P. C. Taylor , Chem. Commun ., 2008, 2807.
O. Miyata et al . Tetrahedron . 2000, 56, 6199-6207
M. Folić, C. S. Adjiman and E.N. Pistikopoulos, Ind. Eng.Chem. Res. 2008, 47, 5190-51
4. Conclusion
Dimethyl carbonate and diethyl ether give a very good yield compared to the other solvents and these can be considered ideal for RCM . To draw a firm conclusion, further studies such as the study of kinetics of RCM reaction in these solvents needs to be done
Substrate | Product | Solvent | Yield [%] | Time / h
Rational selection of solvents for chemical processes
By Mary Kyobula (m.kyobula@wawick.ac.uk). Supervised by Dr. Paul Taylor